I. Create a simple topology of two nodes (Node1, Node2) separated by a point-to-point link. Setup a UdpClient on one Node1 and a UdpServer on Node2. Let it be of a fixed data rate Rate1. Start the client application, and measure end to end throughput whilst varying the latency of the link. Now add another client application to Node1 and a server instance to Node2 and measure the throughput.

II. Create a topology of 7 nodes (n0, n1, n2, n3, n4, n5,n6), as shown in figure below:

// Wifi 10.1.3.0
// AP
// * * * *
// | | | | 10.1.1.0
// n5 n6 n7 n0 -------------- n1 n2 n3 n4
// point-to-point | | | |
// ================
// LAN 10.1.2.0

Node n0 is the sink for all the other nodes. Generate appropriate data from the nodes. Calculate average throughput and delay in the network.

III. Setup a 5x5 wireless adhoc network with a grid. You may use examples/wireless/wifi-simple-adhoc-grid.cc as a base.
  - Install the OLSR routing protocol.
  - Setup three UDP traffic flows, one along each diagonal and one along the middle (at high rates of transmission).
  - Setup the ns-3 flow monitor for each of these flows.
  - Now schedule each of the flows at times 1s, 1.5s, and 2s.
  - Now using the flow monitor, observe the throughput of each of the UDP flows.
  - Now repeat the experiment with RTS/CTS enabled on the wifi devices.
  - Show the difference in throughput and packet drops if any.